## Slide 1
Training-Time Architecture vs. Inference-Time Architecture
Why One Accelerator Cannot Efficiently Do Both
A Survey of Architectural Specialization for AI Workloads
CECS 530 - Advanced Computer Architecture I | Project 8
Presented by: Karthik Kovi, Mohit Krishna Emani, Abishek Mannam

## Slide 2
Presentation Outline
1. Introduction and Background
2. Motivation - Why This Matters
3. Problem Statement
4. Research Focus - Comparison Dimensions
5. Related Research - Reference Implementations (5 systems)
6. Comparative Analysis of All Proposed Solutions
7. Implementation & Results
8. Conclusion
9. References

## Slide 3
1. What is Training?
Training teaches by adjusting parameters (weights) to minimize error.
Three phases: Forward pass (predictions), Backward pass (compute gradients), Optimizer step (Adam update).
Processes huge batches (e.g. 512–2048) simultaneously to keep GPU active.
A single training run costs millions in compute.
Critically Needs: Massive Tensor Core compute + High Memory Capacity.
Training Memory Footprint | Size (1.5B)
Weights (BF16) | 3.0 GB
Gradients (BF16) | 3.0 GB
Optimizer states (FP32) | 18.0 GB
Activations (B=512) | 12–30 GB
Total | 36–54 GB

## Slide 4
1. What is Inference?
Inference is using the trained model to make predictions (autoregressive token generation).
Two phases: Prefill (process whole prompt) and Decode (generate output one by one).
Decode phase bottleneck: Cannot parallelize across output tokens.
No gradients, no optimizer states.
New structure: KV-cache to avoid recomputation of attention states.
Inference Memory Footprint | Size (1.5B INT8)
Weights (INT8) | 1.5 GB
KV-cache (B=1, S=2048) | 0.6 GB
KV-cache (B=32, S=2048) | 20.1 GB
Gradients / Optimizer | None
Total (B=1) | ~2.1 GB

## Slide 5
Key Architecture Terminology
Term | What It Means
FLOPS | Floating-point operations per second (Compute Peak).
Memory Bandwidth | GB/s of data moving between logic and memory.
Arithmetic Intensity (AI) | FLOPs/bytes of memory traffic (crucial metric).
Roofline Model | Plots achievable performance based on AI and limits.
BF16 / INT8 / INT4 | Precision formats. Smaller = less memory bandwidth used.
KV-Cache | Stored keys/values from past inference tokens.
HBM vs SRAM | HBM is external large capacity. SRAM is ultra-fast on-chip logic.

## Slide 6
2. Motivation - The Economic Argument
Inference accounts for 90%+ of total compute hours in production.
Using training hardware for inference is exceptionally wasteful:
A training GPU uses <1% of its compute during inference decode.
The chip still draws huge power (300W+) while idle.
Opportunity: Purpose-built inference ASICs can be drastically cheaper and save 7–9× on TCO.
Cost Breakdown | H100 | Inference ASIC
Chips needed | 12 | 9
Hardware cost | $360K | $27K
3-year TCO | ~$400K | ~$28K
Result | Baseline | ~14× cheaper

## Slide 7
2. Motivation - The Technical Mismatch
Dimension | Training Needs | Inference Needs | Conflict
Primary bottleneck | Compute (FLOPS) | Memory bandwidth | Opposing limits
Batch size | Large: 512–2048 | Small: 1–64 | Opposing configs
Precision | BF16 / FP32 | INT4 / INT8 | Different ALUs
Memory contents | Huge (Weights+Gradients+Adam) | Small (Weights+KV) | Capacity vs BW
Parallelism | Data/Tensor/Pipeline (NVLink) | Minimal | Wasted interconnect
Power budget | 400–700W is okay | 50–100W desired | Different cooling

## Slide 8
3. Problem Statement
Can a single hardware accelerator efficiently serve both training and inference workloads for massive LLMs?
We analyze this question through three metrics:
(a) Workload characterization - quantify AI, memory, and control differences.
(b) Architecture evaluation - map H100 vs Inference-ASIC successes and failures.
(c) Specialized design - evaluate the efficiency gap between setups.
We survey 5 reference implementations (Megatron, DeepSpeed, vLLM, llama.cpp, TVM) to support this architectural divide.

## Slide 9
4. Research Focus - Comparison Dimensions
Parallelism Structure: Training spans GPUs via NVLink; inference is constrained.
Memory Behavior: Training needs static capacity; inference needs dynamic KV paging.
Precision & Numerics: Training requires BF16 gradient stability; inference quantizes.
Control Flow: Training is a static graph; inference is totally dynamic.
Optimization Objective: Training seeks total throughput; inference seeks token latency.

## Slide 10
5. Related Research
Reference Implementations

## Slide 11
Megatron-LM - Training at Scale
Problem: Massive models (billions of parameters) do not fit on a single GPU's memory.
Solution: Intra-layer tensor parallelism. Splits individual weight matrices across GPUs. Calculates portions of the GEMM then combines via AllReduce.
Results: Scaled GPT architectures across 512 GPUs with 76% scaling efficiency and near Peak PFLOPS.
Architectural Needs: Demonstrates that training requires 600+ GB/s high-bandwidth device interconnects (NVLink) to mask communication latency.

## Slide 12
DeepSpeed ZeRO - Memory-Efficient Training
Problem: Standard data parallelism wastes memory by forcing every GPU to store full copies of optimizer states and gradients (e.g. 84 GB per GPU for a 7B model).
Solution: ZeRO (Zero Redundancy Optimizer) partitions optimizer states, gradients, and weights across GPUs.
Results: Enables training up to 1 Trillion parameters. Linear memory scaling with a 1.5× communication cost penalty.
Architectural Needs: Validates that during training, High Memory Capacity and Interconnect Bandwidth are the absolutely critical limiters.

## Slide 13
vLLM - Inference Memory Management
Problem: KV-cache grows dynamically per request. Traditional pre-allocation wastes 60–80% of GPU memory via fragmentation, choking throughput.
Solution: PagedAttention. Borrows OS virtual memory concepts to store KV-cache in non-contiguous, dynamic pages.
Results: 2-4× higher serving throughput than FasterTransformer with near-zero waste.
Architectural Needs: Inference chips need dynamic memory management (paging, eviction) which is totally absent in static training logic.

## Slide 14
llama.cpp - Quantized Inference Everywhere
Problem: Inference is inherently memory-bandwidth-bound, leaving GPU compute idle. Can simpler hardware do the job?
Solution: Pure C/C++ backend doing aggressive INT4 quantization to reduce memory traffic by 4×.
Results: Runs LLaMA-7B smoothly on a MacBook M1 with <1% perplexity loss.
Architectural Insight: Proves that for inference, reducing data movement (BW) matters far more than throwing useless 300+ TFLOP architectures at the problem.

## Slide 15
TVM - Compiler Infrastructure
Problem: Hand-tuning DL operations for diverse heterogeneous hardware is impossible.
Solution: An automated end-to-end optimizing compiler with a learned cost model to search instruction spaces.
Results: Matches or exceeds hand-tuned C++/CUDA libraries.
Architectural Insight: Software compilers can squeeze the hardware entirely, but they can not break the physical Roofline. Software cannot make a compute-heavy chip efficient at a memory-heavy task.

## Slide 16
Comparative Analysis of Surveyed Systems
System | Focus | Key Technique | Perf. Gain | HW Req.
Megatron-LM | Training | Tensor parallelism | 76% scaling | NVLink 600 GB/s
DeepSpeed | Training | ZeRO Sharding | 10× memory save | HBM+Interconnect
vLLM | Inference | PagedAttention | 2-4× throughput | Dynamic Paging HW
llama.cpp | Inference | Quantization | 4× BW cut | INT4 / INT8 ALUs
TVM | Compiler | Auto-compiling | Peak logic fit | Flexible backend
Pattern: Training systems optimize scaling and memory capacity via NVLink. Inference systems optimize dynamic scheduling and pure bandwidth.

## Slide 17
7. Implementation & Results
Analytical framework

## Slide 18
Implementation - Framework
A configurable Python analytical roofline framework matching the Llama 3 8B Hyperparameters.
Llama 3 8B Parameters: 4096 hidden size, 32 layers, Generative Decoder.
Calculates mathematically rigorous Arithmetic Intensity and Memory Access boundaries based on structural hyperparameters rather than theoretical benchmarks.
Simulates Training-Time (H100) vs Inference-Time (Specialized ASIC).

## Slide 19
FLOP Counting Model - 6P vs 2P
Training FLOPs per token: 6 × P = 48.18 × 10⁹ (forward + backward + optimizer)
Inference FLOPs per token: 2 × P = 16.06 × 10⁹ (forward pass only)
P = ~8.03B parameters (Llama 3 8B config)
Per-token FLOPs from python framework:
Training reads are heavily amortized across B=4096.
Inference reads demand massive unamortized weight loading.
Math proves a 53× gap in arithmetic intensity (1,103 vs 20.85 ops/byte)

## Slide 20
Memory Traffic Model
Training Memory Traffic (per token):
Weights: P × (precision_bytes + optimizer_bytes) / B
Amortized to ~19.6 MB/token.
Activations addition: ~9.6 MB/token.
Inference Memory Traffic (per token):
Weight loading is pure memory bottleneck: 8.03B × 1 (INT8) / 16 (Batch) = 501.8 MB/token
KV-cache read addition: ~268 MB/token
Key Insight: Training is amortized by batch size making it compute-bound. Inference is dominated by KV-cache and weights making it pure memory-bound.

## Slide 21
Bottleneck Model - Roofline Evaluation
Algorithm (computed automatically for all configurations):
- compute_bound_toks/s = peak_flops / flops_per_token
- mem_bound_toks/s = bandwidth / bytes_per_token
- effective_throughput = min(compute_bound, mem_bound)
Energy Model:
- power = TDP × 0.4 (static) + 60% dynamic
- energy = power / effective_throughput
- EDP = energy × (1 / effective_throughput)
Example (H100 Inference): Compute capacity is 61,580 tok/s, but limited to 4,348 tok/s by bandwidth. Yields 93% idle silicon compute waste!

## Slide 22
Framework Design - 4 Modules, YAML-Driven
Module | Path | Responsibility
Workload Models | src/workload/ (models, memory, precision, parallelism) | FLOP counting, memory traffic, parallelism taxonomy
Architecture Models | src/architecture/ (models, roofline) | Architecture dataclasses, roofline evaluation
Analysis | src/analysis/ (workload_characterization, architecture_evaluation) | Workload characterization, arch evaluation, bottleneck determination
Metrics | src/metrics/ (training_metrics, inference_metrics) | EDP, TCO, energy-per-token, throughput metrics
Config-Driven Architecture
config/architectures.yaml → defines 3 accelerators
config/workloads.yaml → defines training + inference
config/experiments.yaml → which combos to evaluate
scripts/run_experiments.py → produces JSON results
scripts/benchmark_apple_silicon.py → M4 Pro benchmarks
project8_analysis.py: standalone analytical script
Defines Llama 3 8B model architecture
Instantiates all 3 architectures from params
Runs roofline_throughput() for every pair
Outputs arithmetic intensity, throughput,
energy/token, EDP, cost/million tokens
Notes: Our framework has four Python modules in src/: workload, architecture, analysis, and metrics. Everything is parameterized via three YAML files in config/. The entry point scripts/run_experiments.py loads configs and produces JSON output in results/.
The standalone project8_analysis.py can also run the full evaluation independently, defining the Llama 3 8B model and all three architectures inline. This dual-entry design ensures reproducibility - change a YAML parameter and re-run to see the impact.

## Slide 23
Real Hardware Validation - Apple M4 Pro
Matrix multiplication benchmark (Metal 4) simulating LLM hidden dimensions (N=4096).
Apple Silicon Unified Memory (UMA) provides ~273 GB/s directly to the GPU logic.
Validates our thesis: High bandwidth enables incredible hardware utilization.
Matrix Size (N) | Achieved TFLOP/s | Result
2048 | 6.48 | Excellent
4096 | 6.73 | Peak
8192 | 6.16 | Scale-down

## Slide 24
Full Results Table
Configuration | Compute tok/s | Mem tok/s | Bottleneck | Effective tok/s | Energy (mJ/tok) | EDP (µJ·s) | $/1M tok
H100 / Training | 20,527 | 76,718 | Compute | 20,527 | 34.10 | 1.66 | $0.0164
ASIC / Training | 8,302 | 343,511 | Compute | 8,302 | 9.03 | 1.09 | $0.0041
Unified / Training | 15,213 | 19,786 | Compute | 15,213 | 23.01 | 1.51 | $0.0076
H100 / Inference | 61,580 | 4,348 | Memory | 4,348 | 160.98 | 37.02 | $0.0774
ASIC / Inference | 24,906 | 19,471 | Memory | 19,471 | 3.85 | 0.20 | $0.0017
Unified / Inference | 45,640 | 1,122 | Memory | 1,122 | 312.08 | 278.27 | $0.1029
Training: all architectures are compute-bound — H100 is fastest (20,527 tok/s) due to highest FLOP/s. Inference: all architectures are memory-bound — ASIC is fastest (19,471 tok/s) due to 15 TB/s SRAM BW. Unified-GPU is worst for inference: only 1,122 tok/s due to GDDR6 bandwidth bottleneck (864 GB/s).
Notes: This table shows every result from our framework.
Training rows: all compute-bound. H100 leads at 20,527 tok/s because it has the highest BF16 compute. The Inference-ASIC is slowest for training (8,302 tok/s) — it was never designed for this.
Inference rows: all memory-bound. The ASIC leads at 19,471 tok/s thanks to its 15 TB/s SRAM bandwidth. The H100 achieves only 4,348 tok/s — its 989 TFLOP/s compute is almost entirely wasted. The Unified-GPU is worst at 1,122 tok/s because GDDR6 at 864 GB/s severely limits throughput.
Every number comes from results_20260304_221623.json.

## Slide 25
TCO Analysis - Cost per Million Tokens
3-year TCO = chip_cost + electricity (TDP × 26,280 hours × $0.10/kWh). Cost/1M tokens = TCO / total_tokens.
Architecture | Chip Cost | 3yr Electricity | 3yr TCO | Inference $/1M tok | Training $/1M tok
Training-GPU (H100) | $30,000 | $18,396 | $48,396 | $0.0774 | $0.0164
Inference-ASIC | $3,000 | $1,971 | $4,971 | $0.0017 | $0.0041
Unified-GPU (L40S) | $10,000 | $9,198 | $19,198 | $0.1029 | $0.0076
Inference Cost Comparison
Inference-ASIC: $0.0017/1M tok
H100-class: $0.0774/1M tok → 45× more expensive
Unified L40S: $0.1029/1M tok → 61× more expensive
ASIC advantage: 10× cheaper chip + 9.3× less power
Deployment Recommendations
Workload | Best Architecture
Large-scale training | H100 (highest BF16 TFLOP/s)
Inference serving | ASIC (45× cheaper, 185× better EDP)
Avoid for inference | Unified-GPU (worst EDP, highest cost)
Notes: Our TCO model computes 3-year costs including electricity at $0.10/kWh.
For inference: the ASIC costs $0.0017/1M tokens vs $0.0774 for H100 - 45× cheaper. This comes from both the 10× cheaper chip ($3K vs $30K) and 9.3× less power (75W vs 700W).
The Unified-GPU is actually the most expensive for inference at $0.1029/1M tok - even worse than the H100 - because its low bandwidth yields only 1,122 tok/s.
For training, the H100 is cheapest per token ($0.0164) due to highest throughput. The recommendation is clear: specialize your hardware for the workload.

## Slide 26
Can One Chip Do Both? (Unified Critique)
Requirement | Training Opt | Inference Opt | Conflict
Compute | Max FLOPS | Right-size | Opposing Logic
Memory | 80-96 GB HBM | 20-30 GB HBM | 2-3x Capacity Cost Waste
Interconnect | Heavy NVLink | Minimal | Dead silicon during decoding
Power | 500W okay | 75W needed | 5x mismatch
Conclusion: A unified chip carries the massive cost overhead of both domains, but can only utilize one at a time. This results in 95-99% compute waste during decodes.

## Slide 27
Core Conclusions
1. Training is Compute Bound (1103 ops/byte). Inference is fundamentally Memory Bound (20.8 ops/byte).
2. Training Hardware (H100) mathematically wastes 99% of its resources waiting for streaming inferences.
3. Surveyed frameworks confirm this: Megatron scales Compute. llama.cpp scales Bandwidth.
4. Specialized hardware natively outputs a 185× better EDP, driving TCO down by 45×.
5. The entire AI industry is permanently bifurcating hardware development to match these exact metrics.

## Slide 28
References
[1] Megatron-LM: github.com/NVIDIA/Megatron-LM (Project 8 reference)
[2] DeepSpeed: github.com/microsoft/DeepSpeed (Project 8 reference)
[3] vLLM: github.com/vllm-project/vllm (Project 8 reference)
[4] llama.cpp: github.com/ggerganov/llama.cpp (Project 8 reference)
[5] TVM: github.com/apache/tvm (Project 8 reference)
[6] Shoeybi et al., 'Training Multi-Billion Parameter...'
[7] Kwon et al., 'Efficient Memory Management for LLM...'
[8] Apple inc, 'Unified Memory Architecture on Silicon'

## Slide 29
Thank You
Questions?
Project 8 - Training-Time vs Inference-Time Architecture